## Slide 1: Y86-64 Processor Architecture: Pipelined Implementation COMP 222: Introduction to Computer Organization
Carnegie Mellon
Instructor:
Alan L. Cox

## Slide 2: Overview
General Principles of Pipelining
  Goal
  Difficulties
Creating a Pipelined Y86-64 Processor
  Rearranging SEQ
  Inserting pipeline registers
  Problems with data and control hazards

## Slide 3: Real-World Pipelines: Ford Model T Moving Assembly Line
Idea
  Divide process into independent stages
  Move objects through stages in sequence
  At any given times, multiple objects being processed

## Slide 4: Computational Example
System
  Computation requires total of 300 picoseconds
  Additional 20 picoseconds to save result in register
  Must have clock cycle of at least 320 ps
Combinational
logic
R
e
g
300 ps
20 ps
Clock
Delay = 320 ps
Throughput = 3.12 GIPS

## Slide 5: 3-Way Pipelined Version
System
  Divide combinational logic into 3 blocks of 100 ps each
  Can begin new operation as soon as previous one passes through stage A.
    Begin new operation every 120 ps
  Overall latency increases
    360 ps from start to finish
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Delay = 360 ps
Throughput = 8.33 GIPS

## Slide 6: Pipeline Diagrams
Unpipelined
  Cannot start new operation until previous one completes
3-Way Pipelined
  Up to 3 operations in process simultaneously
Time
OP1
OP2
OP3
Time
A
B
C
A
B
C
A
B
C
OP1
OP2
OP3

## Slide 7: Operating a Pipeline
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C
0
120
240
360
480
640
Clock
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
239
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
241
R
e
g
R
e
g
R
e
g
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Comb.
logic
A
Comb.
logic
B
Comb.
logic
C
Clock
300
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
359

## Slide 8: Limitations: Nonuniform Delays
  Throughput limited by slowest stage
  Other stages sit idle for much of the time
  Challenging to partition system into balanced stages
R
e
g
Clock
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
50 ps
20 ps
150 ps
20 ps
100 ps
20 ps
Delay = 510 ps
Throughput = 5.88 GIPS
Comb.
logic
A
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C

## Slide 9: Limitations: Register Overhead
  As try to deepen pipeline, overhead of loading registers becomes more significant
  Percentage of clock cycle spent loading register:
    1-stage pipeline: 6.25%
    3-stage pipeline: 16.67%
    6-stage pipeline: 28.57%
  High speeds of modern processor designs obtained through very deep pipelining
Delay = 420 ps, Throughput = 14.29 GIPS
Clock
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps
R
e
g
Comb.
logic
50 ps
20 ps

## Slide 10: Data Dependencies
System
  Each operation depends on result from preceding one
Clock
Combinational
logic
R
e
g
Time
OP1
OP2
OP3

## Slide 11: Data Hazards
  Result does not feed back around in time for next operation
  Pipelining has changed behavior of system
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C
OP4
A
B
C

## Slide 12: Data Dependencies in Processors
  Result from one instruction used as operand for another
    Read-after-write (RAW) dependency
  Very common in actual programs
  Must make sure our pipeline handles these properly
    Get correct results
    Minimize performance impact
1 irmovq $50, %rax
2 addq %rax , %rbx
3 mrmovq 100( %rbx ), %rdx

## Slide 13: SEQ Hardware
  Stages occur in sequence
  One operation in process at a time

## Slide 14: SEQ+ Hardware
  Still sequential implementation
  Reorder PC stage to put at beginning
PC Stage
  Task is to select PC for current instruction
  Based on results computed by previous instruction
Processor State
  PC is no longer stored in register
  But, can determine PC based on other stored information

## Slide 15: Adding Pipeline Registers
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 16: Pipeline Stages
Fetch
  Select current PC
  Read instruction
  Compute incremented PC
Decode
  Read program registers
Execute
  Operate ALU
Memory
  Read or write data memory
Write Back
  Update register file

## Slide 17: PIPE- Hardware
  Pipeline registers hold intermediate values from instruction execution
Forward (Upward) Paths
  Values passed from one stage to next
  Cannot jump past stages
    e.g., valC passes through decode

## Slide 18: Signal Naming Conventions
S_Field
  Value of Field held in stage S pipeline register
s_Field
  Value of Field computed in stage S

## Slide 19: Feedback Paths
Predicted PC
  Guess value of next PC
Branch information
  Jump taken/not-taken
  Fall-through or target address
Return point
  Read from memory
Register updates
  To register file write ports

## Slide 20: Predicting the PC
  Start fetch of new instruction after current one has completed fetch stage
    Not enough time to reliably determine next instruction
  Guess which instruction will follow
    Recover if prediction was incorrect

## Slide 21: Our Prediction Strategy
Instructions that Don’t Transfer Control
  Predict next PC to be valP
  Always reliable
Call and Unconditional Jumps
  Predict next PC to be valC (destination)
  Always reliable
Conditional Jumps
  Predict next PC to be valC (destination)
  Only correct if branch is taken
    Typically right 60% of time
Return Instruction
  Don’t try to predict

## Slide 22: Recovering from PC Misprediction
  Mispredicted Jump
    Will see branch condition flag once instruction reaches memory stage
    Can get fall-through PC from valA (value M_valA)
  Return Instruction
    Will get return PC when ret reaches write-back stage (W_valM)

## Slide 23: Pipeline Demonstration
File: demo-basic.ys
irmovq $1,%rax #I1
1
2
3
4
5
6
7
8
9
F
D
E
M
W
irmovq $2,%rcx #I2
F
D
E
M
W
irmovq $3,%rdx #I3
F
D
E
M
W
irmovq $4,%rbx #I4
F
D
E
M
W
halt #I5
F
D
E
M
W
Cycle 5
W
I1
M
I2
E
I3
D
I4
F
I5

## Slide 24: Data Dependencies: 3 Nop’s
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
nop
F
D
E
M
W
F
D
E
M
W
0x015:
nop
F
D
E
M
W
F
D
E
M
W
0x016:
nop
F
D
E
M
W
F
D
E
M
W
0x017:
addq
%
rdx
,%
rax
F
D
E
M
W
F
D
E
M
W
10
W
R[
%
rax
]
f
3
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
3
# demo-h3.ys
Cycle 6
11
0x019: halt
F
D
E
M
W
F
D
E
M
W
Cycle 7

## Slide 25: Data Dependencies: 2 Nop’s
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
nop
F
D
E
M
W
F
D
E
M
W
0x015:
nop
F
D
E
M
W
F
D
E
M
W
0x016:
addq
%
rdx
,%
rax
F
D
E
M
W
F
D
E
M
W
0x018: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-h2.ys
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
•
•
•
W
R[
%
rax
]
f
3
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
•
•
•
Cycle 6
Error

## Slide 26: Data Dependencies: 1 Nop
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
0x014:
nop
F
D
E
M
W
F
D
E
M
W
0x015:
addq
%
rdx
,%
rax
F
D
E
M
W
F
D
E
M
W
0x017: halt
F
D
E
M
W
F
D
E
M
W
# demo-h1.ys
W
R[
%
rdx
]
f
10
W
R[
%
rdx
]
f
10
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
•
•
•
Cycle 5
Error
M
M_
valE
= 3
M_
dstE
=
%
rax

## Slide 27: Data Dependencies: No Nop
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
addq
%
rdx
,%
rax
F
D
E
M
W
0x016: halt
# demo-h0.ys
E
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
Cycle 4
Error
M
M_
valE
= 10
M_
dstE
=
%
rdx
e_
valE
f
0 + 3 = 3
E_
dstE
=
%
rax

## Slide 28: Branch Misprediction Example
  Should only execute first 8 instructions
0x000: xorq %rax,%rax
0x002: jne t # Not taken
0x00b: irmovq $1, %rax # Fall through
0x015: nop
0x016: nop
0x017: nop
0x018: halt
0x019: t: irmovq $3, %rdx # Target (Should not execute)
0x023: irmovq $4, %rcx # Should not execute
0x02d: irmovq $5, %rdx # Should not execute
demo-j.ys

## Slide 29: Branch Misprediction Trace
  Incorrectly execute two instructions at branch target
0x000:
xorq
%
rax
,%
rax
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x002:
jne
t # Not taken
F
D
E
M
W
0x019: t:
irmovq
$3, %
rdx
# Target
F
D
E
M
W
0x023:
irmovq
$4, %
rcx
# Target+1
F
D
E
M
W
0x00b:
irmovq
$1, %
rax
# Fall Through
F
D
E
M
W
# demo
-
j
F
D
E
M
W
Cycle 5
E
valE
f
3
dstE
=
%
rdx
E
valE
f
3
dstE
=
%
rdx
M
M_Cnd =
0
M_
valA
= 0x007
D
valC
=
4
dstE
=
%
ecx
D
valC
=
4
dstE
=
%
rcx
F
valC
f
1
rB
f
%
rax
F
valC
f
1
rB
f
%
rax

## Slide 30: Return Example
0x000: irmovq Stack,%rsp # Intialize stack pointer
0x00a: nop # Avoid hazard on %rsp
0x00b: nop
0x00c: nop
0x00d: call p # Procedure call
0x016: irmovq $5,%rsi # Return point
0x020: halt
0x020: .pos 0x20
0x020: p: nop # procedure
0x021: nop
0x022: nop
0x023: ret
0x024: irmovq $1,%rax # Should not be executed
0x02e: irmovq $2,%rcx # Should not be executed
0x038: irmovq $3,%rdx # Should not be executed
0x042: irmovq $4,%rbx # Should not be executed
0x100: .pos 0x100
0x100: Stack: # Initial stack pointer
  Require lots of nops to avoid data hazards
demo-ret.ys

## Slide 31: Incorrect Return Example
  Incorrectly execute 3 instructions following ret

## Slide 32: Pipeline Summary
Concept
  Break instruction execution into 5 stages
  Run instructions through in pipelined mode
Limitations
  Can’t handle dependencies between instructions when instructions follow too closely
  Data dependencies
    One instruction writes register, later one reads it
  Control dependency
    Instruction sets PC in way that pipeline did not predict correctly
    Mispredicted branch and return
Fixing the Pipeline
  We’ll do that next time

## Slide 33: Part Two Overview
  Make the pipelined processor work!
Data Hazards
  Instruction having register R as source follows shortly after instruction having register R as destination
  Common condition, don’t want to slow down pipeline
Control Hazards
  Mispredict conditional branch
    Our design predicts all branches as being taken
    Naïve pipeline executes two extra instructions
  Getting return address for ret instruction
    Naïve pipeline executes three extra instructions
Making Sure It Really Works
  What if multiple special cases happen simultaneously?

## Slide 34: Pipeline Stages
Fetch
  Select current PC
  Read instruction
  Compute incremented PC
Decode
  Read program registers
Execute
  Operate ALU
Memory
  Read or write data memory
Write Back
  Update register file

## Slide 35: PIPE- Hardware
  Pipeline registers hold intermediate values from instruction execution
Forward (Upward) Paths
  Values passed from one stage to next
  Cannot jump past stages
    e.g., valC passes through decode

## Slide 36: Data Dependencies: 2 Nop’s
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
nop
F
D
E
M
W
F
D
E
M
W
0x015:
nop
F
D
E
M
W
F
D
E
M
W
0x016:
addq
%
rdx
,%
rax
F
D
E
M
W
F
D
E
M
W
0x018: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-h2.ys
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
•
•
•
W
R[
%
rax
]
f
3
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
•
•
•
Cycle 6
Error

## Slide 37: Data Dependencies: No Nop
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
addq
%
rdx
,%
rax
F
D
E
M
W
0x016: halt
# demo-h0.ys
E
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
Cycle 4
Error
M
M_
valE
= 10
M_
dstE
=
%
rdx
e_
valE
f
0 + 3 = 3
E_
dstE
=
%
rax

## Slide 38: Stalling for Data Dependencies
  If instruction follows too closely after one that writes register, slow it down
  Hold instruction in decode
  Dynamically inject nop into execute stage
0x000: irmovq $10,%rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x00a: irmovq $3,%rax
F
D
E
M
W
0x014: nop
F
D
E
M
W
bubble
F
E
M
W
0x016: addq %rdx,%rax
D
D
E
M
W
0x018: halt
F
D
E
M
W
10
# demo-h2.ys
F
F
D
E
M
W
0x015: nop
11

## Slide 39: Stall Condition
Source Registers
  srcA and srcB of current instruction in decode stage
Destination Registers
  dstE and dstM fields
  Instructions in execute, memory, and write-back stages
Special Case
  Don’t stall for register ID 15 (0xF)
    Indicates absence of register operand
    Or failed cond. move

## Slide 40: Detecting Stall Condition
0x000: irmovq $10,%rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x00a: irmovq $3,%rax
F
D
E
M
W
0x014: nop
F
D
E
M
W
bubble
F
E
M
W
0x016: addq %rdx,%rax
D
D
E
M
W
0x018: halt
F
D
E
M
W
10
# demo-h2.ys
F
F
D
E
M
W
0x015: nop
11
Cycle 6
W
D
•
•
•
W_dstE = %rax
W_valE = 3
srcA = %rdx
srcB = %rax

## Slide 41: Stalling X3
0x000: irmovq $10,%rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x00a: irmovq $3,%rax
F
D
E
M
W
bubble
F
E
M
W
bubble
D
E
M
W
0x014: addq %rdx,%rax
D
D
E
M
W
0x016: halt
F
D
E
M
W
10
# demo-h0.ys
F
F
D
F
E
M
W
bubble
11
Cycle 4
•
•
•
W
W_dstE = %rax
D
srcA = %rdx
srcB = %rax
•
•
•
M
M_dstE = %rax
D
srcA = %rdx
srcB = %rax
E
e_dstE = %rax
D
srcA = %rdx
srcB = %rax
Cycle 5
Cycle 6

## Slide 42: What Happens When Stalling?
  Stalling instruction held back in decode stage
  Following instruction stays in fetch stage
  Bubbles injected into execute stage
    Like dynamically generated nop’s
    Move through later stages
0x000: irmovq $10,%rdx
0x00a: irmovq $3,%rax
0x014: addq %rdx,%rax
Cycle 4
0x016: halt
0x000: irmovq $10,%rdx
0x00a: irmovq $3,%rax
0x014: addq %rdx,%rax
# demo-h0.ys
0x016: halt
0x000: irmovq $10,%rdx
0x00a: irmovq $3,%rax
bubble
0x014: addq %rdx,%rax
Cycle 5
0x016: halt
0x00a: irmovq $3,%rax
bubble
0x014: addq %rdx,%rax
bubble
Cycle 6
0x016: halt
bubble
bubble
0x014: addq %rdx,%rax
bubble
Cycle 7
0x016: halt
bubble
bubble
Cycle 8
0x014: addq %rdx,%rax
0x016: halt
Write Back
Memory
Execute
Decode
Fetch

## Slide 43: Implementing Stalling
Pipeline Control
  Combinational logic detects stall condition
  Sets mode signals for how pipeline registers should update
Pipeline
control
logic
Pipeline
control
logic
Pipeline
control
logic
Pipeline
control
logic

## Slide 44: Pipeline Register Modes
Rising
clock
Rising
clock
_
_
Output = y
y
y
Rising
clock
Rising
clock
_
_
Output = x
x
x
x
x
n
o
p
Rising
clock
Rising
clock
_
_
Output =
nop
Output = x
Input = y
stall
= 0
bubble
= 0
x
x
Normal
Output = x
Input = y
stall
= 1
bubble
= 0
x
x
Stall
Output = x
Input = y
stall
= 0
bubble
= 1
Bubble

## Slide 45: Data Forwarding
Naïve Pipeline
  Register isn’t written until completion of write-back stage
  Source operands read from register file in decode stage
    Needs to be in register file at start of stage
Observation
  Value generated in execute or memory stage
Trick
  Pass value directly from generating instruction to decode stage
  Needs to be available at end of decode stage

## Slide 46: Data Forwarding Example
  irmovq in write-back stage
  Destination value in W pipeline register
  Forward as valB for decode stage
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
nop
F
D
E
M
W
F
D
E
M
W
0x015:
nop
F
D
E
M
W
F
D
E
M
W
0x016:
addq
%
rdx
,%
rax
F
D
E
M
W
F
D
E
M
W
0x018: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-h2.ys
Cycle 6
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
W_
valE
=
3
•
•
•
W_
dstE
=
%
rax
W_
valE
= 3
srcA
=
%
rdx
srcB
=
%
rax

## Slide 47: Bypass Paths
Decode Stage
  Forwarding logic selects valA and valB
  Normally from register file
  Forwarding: get valA or valB from later pipeline stage
Forwarding Sources
  Execute: valE
  Memory: valE, valM
  Write back: valE, valM

## Slide 48: Data Forwarding Example #2
Register %rdx
  Generated by ALU during previous cycle
  Forward from memory as valA
Register %rax
  Value just generated by ALU
  Forward from execute as valB
0x000: irmovq $10,%rdx
1
2
3
4
5
6
7
8
F
D
E
M
W
0x00a: irmovq $3,%rax
F
D
E
M
W
F
D
E
M
W
0x014: addq %rdx,%rax
F
D
E
M
W
0x016: halt
# demo-h0.ys
Cycle 4
M
D
valA f M_valE = 10
valB f e_valE = 3
M_dstE = %rdx
M_valE = 10
srcA = %rdx
srcB = %rax
E
E_dstE = %rax
e_valE f 0 + 3 = 3

## Slide 49: Forwarding Priority
Multiple Forwarding Choices
  Which one should have priority
  Match serial semantics
  Use matching value from earliest pipeline stage
0x000: irmovq $1, %rax
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a: irmovq $2, %rax
F
D
E
M
W
F
D
E
M
W
0x014: irmovq $3, %rax
F
D
E
M
W
F
D
E
M
W
0x01e: rrmovq %rax, %rdx
F
D
E
M
W
F
D
E
M
W
0x020: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-priority.ys
W
R[
%
rax
]
f
3
W
R[
%
rax
]
f
1
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
D
valA
f
R[
%
rax
]
=
?
valB
f
0
Cycle 5
W
R[
%
rax
]
f
3
M
R[
%
rax
]
f
2
W
R[
%
rax
]
f
3
E
R[
%
rax
]
f
3

## Slide 50: Implementing Forwarding
  Add additional feedback paths from E, M, and W pipeline registers into decode stage
  Create logic blocks to select from multiple sources for valA and valB in decode stage

## Slide 51: Implementing Forwarding
## What should be the A value?
int d_valA = [
# Use incremented PC
D_icode in { ICALL, IJXX } : D_valP;
# Forward valE from execute
d_srcA == e_dstE : e_valE;
# Forward valM from memory
d_srcA == M_dstM : m_valM;
# Forward valE from memory
d_srcA == M_dstE : M_valE;
# Forward valM from write back d_srcA == W_dstM : W_valM;
# Forward valE from write back
d_srcA == W_dstE : W_valE;
# Use value read from register file
1 : d_rvalA;
];

## Slide 52: Limitation of Forwarding
Load-use dependency
  Value needed by end of decode stage in cycle 7
  Value read from memory in memory stage of cycle 8

## Slide 53: Avoiding Load/Use Hazard
  Stall using instruction for one cycle
  Can then pick up loaded value by forwarding from memory stage

## Slide 54: Detecting Load/Use Hazard
Condition | Trigger
Load/Use Hazard | E_icode in { IMRMOVQ, IPOPQ } && E_dstM in { d_srcA, d_srcB }

## Slide 55: Control for Load/Use Hazard
  Stall instructions in fetch and decode stages
  Inject bubble into execute stage
0x000:
irmovq
$128,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a:
irmovq
$3,%
rcx
F
D
E
M
W
F
D
E
M
W
0x014:
rmmovq
%
rcx
, 0(%
rdx
)
F
D
E
M
W
F
D
E
M
W
0x01e:
irmovq
$10,%
ebx
F
D
E
M
W
F
D
E
M
W
0x028:
mrmovq
0(%
rdx
),
%
rax
# Load %
rax
F
D
E
M
W
F
D
E
M
W
# demo
-
luh
.
ys
0x032:
addq
%
ebx
,
%
rax
# Use %
rax
0x034: halt
F
D
E
M
W
E
M
W
10
D
D
E
M
W
11
bubble
F
D
E
M
W
F
F
12
Condition | F | D | E | M | W
Load/Use Hazard | stall | stall | bubble | normal | normal

## Slide 56: Branch Misprediction Example
  Should only execute first 8 instructions
0x000: xorq %rax,%rax
0x002: jne t # Not taken
0x00b: irmovq $1, %rax # Fall through
0x015: nop
0x016: nop
0x017: nop
0x018: halt
0x019: t: irmovq $3, %rdx # Target
0x023: irmovq $4, %rcx # Should not execute
0x02d: irmovq $5, %rdx # Should not execute
demo-j.ys

## Slide 57: Handling Misprediction
Predict branch as taken
  Fetch 2 instructions at target
Cancel when mispredicted
  Detect branch not-taken in execute stage
  On following cycle, replace instructions in execute and decode by bubbles
  No side effects have occurred yet

## Slide 58: Detecting Mispredicted Branch
Condition | Trigger
Mispredicted Branch | E_icode = IJXX & !e_Cnd

## Slide 59: Control for Misprediction
Condition | F | D | E | M | W
Mispredicted Branch | normal | bubble | bubble | normal | normal

## Slide 60: Return Example
0x000: irmovq Stack,%rsp # Intialize stack pointer
0x00a: call p # Procedure call
0x013: irmovq $5,%rsi # Return point
0x01d: halt
0x020: .pos 0x20
0x020: p: irmovq $-1,%rdi # procedure
0x02a: ret
0x02b: irmovq $1,%rax # Should not be executed
0x035: irmovq $2,%rcx # Should not be executed
0x03f: irmovq $3,%rdx # Should not be executed
0x049: irmovq $4,%rbx # Should not be executed
0x100: .pos 0x100
0x100: Stack: # Stack: Stack pointer
  Previously executed three additional instructions
demo-retb.ys

## Slide 61: Correct Return Example
0x026: ret
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
0x013:
irmovq
$5,%
rsi
# Return
F
D
E
M
W
# demo
-
retb
F
D
E
M
W
F
valC
f
5
rB
f
%
esi
F
valC
f
5
rB
f
%
rsi
W
valM
=
0x0b
W
valM
=
0x013
•
•
•
  As ret passes through pipeline, stall at fetch stage
    While in decode, execute, and memory stage
  Inject bubble into decode stage
  Release stall when reach write-back stage

## Slide 62: Detecting Return
Condition | Trigger
Processing ret | IRET in { D_icode, E_icode, M_icode }

## Slide 63: Control for Return
0x026: ret
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
0x014:
irmovq
$5,%
rsi
# Return
F
D
E
M
W
# demo
-
retb
F
D
E
M
W
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal

## Slide 64: Special Control Cases
Detection
Action (on next cycle)
Condition | Trigger
Processing ret | IRET in { D_icode, E_icode, M_icode }
Load/Use Hazard | E_icode in { IMRMOVQ, IPOPQ } && E_dstM in { d_srcA, d_srcB }
Mispredicted Branch | E_icode = IJXX & !e_Cnd
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Mispredicted Branch | normal | bubble | bubble | normal | normal

## Slide 65: Implementing Pipeline Control
  Combinational logic generates pipeline control signals
  Action occurs at start of following cycle

## Slide 66: Initial Version of Pipeline Control
bool F_stall =
# Conditions for a load/use hazard
E_icode in { IMRMOVQ, IPOPQ } && E_dstM in { d_srcA, d_srcB } ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode };
bool D_stall =
# Conditions for a load/use hazard
E_icode in { IMRMOVQ, IPOPQ } && E_dstM in { d_srcA, d_srcB };
bool D_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Cnd) ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode };
bool E_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Cnd) ||
# Load/use hazard
E_icode in { IMRMOVQ, IPOPQ } && E_dstM in { d_srcA, d_srcB };

## Slide 67: Control Combinations
  Special cases that can arise on same clock cycle
Combination A
  Not-taken branch
  ret instruction at branch target
Combination B
  Instruction that reads from memory to %rsp
  Followed by ret instruction

## Slide 68: Control Combination A
  Should handle as mispredicted branch
  Stalls F pipeline register
  But PC selection logic will be using M_valM anyhow
JXX
E
D
M
Mispredict
JXX
E
D
M
Mispredict
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination A
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Mispredicted Branch | normal | bubble | bubble | normal | normal
Combination | stall | bubble | bubble | normal | normal

## Slide 69: Control Combination B
  Would attempt to bubble and stall pipeline register D
  Signaled by processor as pipeline error
Load
E
Use
D
M
Load/use
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination B
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | bubble + stall | bubble | normal | normal

## Slide 70: Handling Control Combination B
  Load/use hazard should get priority
  ret instruction should be held in decode stage for additional cycle
Load
E
Use
D
M
Load/use
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination B
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | stall | bubble | normal | normal

## Slide 71: Corrected Pipeline Control Logic
  Load/use hazard should get priority
  ret instruction should be held in decode stage for additional cycle
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | stall | bubble | normal | normal
bool D_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Cnd) ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode }
# but not condition for a load/use hazard
&& !(E_icode in { IMRMOVQ, IPOPQ }
&& E_dstM in { d_srcA, d_srcB });

## Slide 72: Pipeline Summary
Data Hazards
  Most handled by forwarding
    No performance penalty
  Load/use hazard requires one cycle stall
Control Hazards
  Cancel instructions when detect mispredicted branch
    Two clock cycles wasted
  Stall fetch stage while ret passes through pipeline
    Three clock cycles wasted
Control Combinations
  Must analyze carefully
  First version had subtle bug
    Only arises with unusual instruction combination