## Slide 1: Dynamic Memory Allocation
Alan L. Cox
alc@rice.edu
Some slides adapted from CMU 15.213 slides

## Slide 2: Objectives
Be able to analyze a dynamic memory allocator’s key characteristics
  Memory usage efficiency (fragmentation)
  Speed of allocation and deallocation operations
  Locality of allocations
  Robustness
Be able to implement your own efficient dynamic memory allocator (Malloc Project)
Be able to analyze the advantages and disadvantages of different garbage collector designs

## Slide 3: Harsh Reality: Memory Matters
Memory is not unbounded
  It must be allocated and freed
  Many applications are memory dominated
    E.g., applications based on complex graph algorithms
    sample.c in this week’s lab spent >50% of its time allocating and freeing memory
Memory referencing bugs especially pernicious
  Effects can be distant in both time and space
Memory performance is not uniform
  Cache and virtual memory effects can greatly affect program performance
  Adapting program to characteristics of memory system can lead to major speed improvements

## Slide 4: Memory Allocation
Static size, static allocation
  Global and static variables
  Linker allocates final addresses
  Executable stores these allocated addresses
Static size, dynamic allocation
  Local variables
  Compiler directs stack allocation
  Frame pointer (%rbp) offsets stored in the code
Dynamic size, dynamic allocation
  Programmer controlled
  Allocated in the heap – how?

## Slide 5: Dynamic Memory Allocation
Explicit vs. implicit memory allocator
  Explicit: application allocates and frees space
    e.g., malloc and free in C
  Implicit: application allocates, but does not free space
    e.g., garbage collection in Java or Python
Allocation
  In both cases the memory allocator provides an abstraction of memory as a set of blocks
  Doles out free memory blocks to application
We will first discuss simple explicit memory allocation
Application
Dynamic Memory Allocator
Heap Memory

## Slide 6: Process Memory Image
void *sbrk(intptr_t incr)
  Easiest to use function for allocators to request additional heap memory from the OS
  brk initially set to the end of the data section
  Calls to sbrk increment brk by incr bytes (new memory is zero filled)
  incr can be negative to reduce the heap size
User Stack
Shared Libraries
Heap
Read/Write Data
Read-only Code and Data
Unused
%rsp
0x00000000
brk

## Slide 7: Malloc Package
#include <stdlib.h>
void *malloc(size_t size)
  If successful:
    Returns a pointer to a memory block of at least size bytes, aligned to at least an 8-byte boundary
    If size == 0, returns NULL (or a unique pointer)
  If unsuccessful: returns NULL (0)
void free(void *ptr)
  Returns the block pointed at by ptr to pool of available memory
  ptr must come from a previous call to malloc or realloc
void *realloc(void *ptr, size_t size)
  Changes size of block pointed at by ptr and returns pointer to new block
  Contents of new block unchanged up to the minimum of the old and new sizes

## Slide 8: Malloc/realloc/free Example
void
foo(int n, int m)
{
int i, *p;
/* Allocate a block of n ints. */
if ((p = malloc(n * sizeof(int))) == NULL)
unix_error("malloc");
for (i = 0; i < n; i++)
p[i] = i;
/* Add m bytes to end of p block. */
if ((p = realloc(p, (n + m) * sizeof(int))) == NULL)
unix_error("realloc");
for (i = n; i < n + m; i++)
p[i] = i;
/* Print new array. */
for (i = 0; i < n + m; i++)
printf("%d\n", p[i]);
/* Return p to available memory pool. */
free(p);
}

## Slide 9: Assumptions
Conventions used in these lectures
  Each “box” in a figure represents a word
  Memory is word addressed
  Each word is 4 bytes in size and can hold an integer or a pointer
Allocated block
(4 words)
Free block
(3 words)
Free word
Allocated word

## Slide 10: Allocation Examples
p1 = malloc(4*sizeof(int))
p2 = malloc(5*sizeof(int))
p3 = malloc(6*sizeof(int))
free(p2)
p4 = malloc(2*sizeof(int))

## Slide 11: Governing Rules
Applications:
  Can issue arbitrary sequence of malloc and free requests
  Free requests must correspond to an allocated block
Allocators:
  Can’t control number or size of allocated blocks
  Must respond immediately to all allocation requests
    i.e., can’t reorder or buffer requests
  Must allocate blocks from free memory
    i.e., can only place allocated blocks in free memory
  Must align blocks so they satisfy all alignment requirements
    e.g., 8-byte alignment for libc malloc on some systems
  Can only manipulate and modify free memory
  Can’t move the allocated blocks once they are allocated
    i.e., compaction is not allowed

## Slide 12: Goals of Good malloc/free
Primary goals
  Good time performance for malloc and free
    Ideally should take constant time (not always possible)
    Should certainly not take linear time in the number of blocks
  Good space utilization
    User allocated structures should use most of the heap
    Want to minimize “fragmentation”
Some other goals
  Good locality properties
    Structures allocated close in time should be close in space
    “Similar” types of objects should be allocated close in space
  Robust
    Can check that free(p1) is on a valid allocated object p1
    Can check that memory references are to allocated space

## Slide 13: Maximizing Throughput
Given some sequence of n malloc, realloc, and free requests:
  R0, R1, ..., Rk, ... , Rn-1
Want to maximize throughput and peak memory utilization
  These goals are often conflicting
Throughput:
  Number of completed requests per unit time
  Example:
    5,000 malloc calls and 5,000 free calls in 10 seconds
    Throughput is 1,000 operations/second

## Slide 14: Maximizing Memory Utilization
Given some sequence of malloc and free requests:
  R0, R1, ..., Rk, ... , Rn-1
Def: Aggregate payload Pk:
  malloc(p) results in a block with a payload of p bytes
  After request Rk has completed, the aggregate payload Pk is the sum of currently allocated payloads
Def: Current heap size is denoted by Hk
  Assume that Hk is monotonically increasing
Def: Peak memory utilization Uk:
  After k requests, peak memory utilization is:
    Uk = ( maxi<k Pi ) / Hk

## Slide 15: Internal Fragmentation
Poor memory utilization caused by fragmentation
  Comes in two forms: internal and external fragmentation
Internal fragmentation
  For some block, internal fragmentation is the difference between the block size and the payload size
  Caused by overhead of maintaining heap data structures, padding for alignment purposes, or explicit policy decisions (e.g., not to split the block)
  Depends only on the pattern of previous requests, and thus is easy to measure
payload
Internal
fragmentation
block
Internal
fragmentation

## Slide 16: External Fragmentation
p4 = malloc(7*sizeof(int))
oops!
Occurs when there is enough aggregate heap memory, but no
single free block is large enough
External fragmentation depends on the pattern of future
requests, and thus is difficult to measure
p1 = malloc(4*sizeof(int))
p2 = malloc(5*sizeof(int))
p3 = malloc(6*sizeof(int))
free(p2)

## Slide 17: Implementation Issues
  How do we know how much memory to free just given a pointer?
  How do we keep track of the free blocks?
  How do we pick a block to use for an allocation?
  What do we do with the extra space when allocating memory for an object that is smaller than the free block it is placed in?
  How do we reinsert a freed block?
p1 = malloc(1)
p0
free(p0)

## Slide 18: Knowing How Much to Free
Standard method
  Keep the length of a block in the word preceding the block.
    This word is often called the header field or header
  Requires an extra word for every allocated block
free(p0)
p0 = malloc(4 * sizeof(int))
p0
Block size
data
5

## Slide 19: Keeping Track of Free Blocks
Method 1: Implicit list using lengths – links all blocks
Method 2: Explicit list among the free blocks using pointers within the free blocks
Method 3: Segregated free list
  Different free lists for different size ranges
Method 4: Blocks sorted by size
  Can use a balanced binary search tree where a node contains the head of an explicit list of free blocks of a single size and that size is used as the key
5
4
2
6
5
4
2
6

## Slide 20: Method 1: Implicit List
Need to identify whether each block is free or allocated
  Can use a single bit
  Bit can be put in the same word as the size if block sizes are always multiples of two (mask out low order bit when reading size)
size
1 word
Format of
allocated and
free blocks
payload
a = 1: allocated block
a = 0: free block
size: block size
payload: application data
(allocated blocks only)
a
optional
padding

## Slide 21: Implicit List: Finding a Free Block
First fit:
  Search list from beginning, choose first free block that fits
  Can take linear time in total number of blocks (allocated/free)
  Can cause “splinters” (small free blocks) at beginning of list
Next fit:
  Like first-fit, but search list from end of previous search
  Research suggests that fragmentation is worse
Best fit:
  Choose the free block with the closest size that fits (requires complete search of the list)
  Keeps fragments small – usually helps fragmentation
  Will typically run slower than first-fit
p = start;
while (p < end && // not past end
((*p & 0x1) != 0 || // already allocated
*p <= len)) // too small
p = p + (*p & ~0x1); // advance to next block

## Slide 22: Implicit List: Allocating in Free Block
Allocating in a free block – splitting
  Since allocated space might be smaller than free space, we might want to split the block
void place_block(ptr p, int len) {
int newsize = ((len + 1) / 2) * 2; // add 1 and round up
int oldsize = *p & ~0x1; // mask out low bit
*p = newsize | 0x1; // set new length
if (newsize < oldsize)
*(p + newsize) = oldsize - newsize; // set length in remaining
} // part of block
4
4
2
6
4
2
4
p
2
4
place_block(p, 4)

## Slide 23: Implicit List: Freeing a Block
Simplest implementation:
  Only need to clear allocated flag
    void free_block(ptr p) { *p = *p & ~0x1; }
  But can lead to “false fragmentation”
  There is enough free space, but the allocator won’t be able to find it!
p
malloc(5 * sizeof(int))
Oops!
free_block(p)
4
4
2
4
2
4
2
4
2
4

## Slide 24: Implicit List: Coalescing
Join (coalesce) with next and/or previous block if they are free
  Coalescing with next block
  But how do we coalesce with previous block?
4
2
4
2
p
4
void free_block(ptr p) { *p = *p & ~0x1; // clear allocated flag next = p + *p; // find next block if ((*next & 0x1) == 0) *p = *p + *next; // add to this block if } // not allocated
free_block(p)
4
4
2
6

## Slide 25: Implicit List: Bidirectional Coalescing
Boundary tags [Knuth73]
  Replicate header word at end of block
  Allows us to traverse the “list” backwards, but requires extra space
  Important and general technique!
size
Format of
allocated and
free blocks
payload and
padding
a = 1: allocated block
a = 0: free block
size: total block size
payload: application data
(allocated blocks only)
a
size
a
Boundary tag
(footer)
4
4
4
4
6
4
6
4
Header

## Slide 26: Constant Time Coalescing
allocated
allocated
allocated
free
free
allocated
free
free
block being
freed
Case 1
Case 2
Case 3
Case 4

## Slide 27: Constant Time Coalescing (Case 1)
m1
1
m1
1
n
1
n
1
m2
1
m2
1
m1
1
m1
1
n
0
n
0
m2
1
m2
1

## Slide 28: Constant Time Coalescing (Case 2)
m1
1
m1
1
n+m2
0
n+m2
0
m1
1
m1
1
n
1
n
1
m2
0
m2
0

## Slide 29: Constant Time Coalescing (Case 3)
m1
0
m1
0
n
1
n
1
m2
1
m2
1
n+m1
0
n+m1
0
m2
1
m2
1

## Slide 30: Constant Time Coalescing (Case 4)
m1
0
m1
0
n
1
n
1
m2
0
m2
0
n+m1+m2
0
n+m1+m2
0

## Slide 31: Implicit Lists: +’s and –’s
Implementation: very simple (“+”)
Allocate: linear time worst case (“-”)
Free: constant time worst case – even with coalescing (“+”)
Memory usage: will depend on placement policy
  First fit, next fit, or best fit

## Slide 32: Implicit Lists: Summary
Not used in practice for malloc/free because of linear time allocate
  Used in some special-purpose applications
However, the concepts of placement, splitting, and boundary tag coalescing are general to all allocators

## Slide 33: Summary of Key Allocator Policies
Placement policy:
  First fit, next fit, or best fit?
  Different throughput versus fragmentation trade offs
Splitting policy:
  When do we go ahead and split free blocks?
  How much internal fragmentation are we willing to tolerate?
Coalescing policy:
  Immediate coalescing: coalesce adjacent blocks each time free is called
  Deferred coalescing: try to improve performance of free by deferring coalescing until needed, e.g.,
    Coalesce as you scan the free list for malloc
    Coalesce when the amount of external fragmentation reaches some threshold

## Slide 34: Keeping Track of Free Blocks
Method 1: Implicit list using lengths – links all blocks
Method 2: Explicit list among the free blocks using pointers within the free blocks
Method 3: Segregated free list
  Different free lists for different size ranges
Method 4: Blocks sorted by size
  Can use a balanced binary search tree where a node contains the head of an explicit list of free blocks of a single size and that size is used as the key
5
4
2
6
5
4
2
6

## Slide 35: Explicit Free Lists
Use data space for link pointers
  Typically doubly linked
  Still need boundary tags for coalescing
  It is important to realize that blocks are not necessarily in the same order in the free list as in the heap
A
B
C
4
4
4
4
6
6
4
4
4
4
Forward links
Back links
A
B
C

## Slide 36: Allocating From Explicit Free Lists
free block
pred
succ
free block
pred
succ
Before:
After:
(with splitting)

## Slide 37: Freeing With Explicit Free Lists
Insertion policy: Where in the free list do you put a newly freed block?
  LIFO (last-in-first-out) policy
    Insert freed block at the beginning of the free list
    Pro: simple and constant time
    Con: studies suggest fragmentation is worse than address ordered
  Address-ordered policy
    Insert freed blocks so that free list blocks are always in address order
      i.e. addr(pred) < addr(curr) < addr(succ)
    Con: requires search
    Pro: studies suggest fragmentation is better than LIFO

## Slide 38: Freeing With a LIFO Policy
Case 1: a-a-a
  Insert self at beginning of free list
Case 2: a-a-f
  Splice out next, coalesce self and next, and add to beginning of free list
self
a
a
p
s
self
a
f
before:
p
s
f
a
after:
h
h

## Slide 39: Freeing With a LIFO Policy (cont)
Case 3: f-a-a
  Splice out prev, coalesce with self, and add to beginning of free list
Case 4: f-a-f
  Splice out prev and next, coalesce with self, and add to beginning of list
p
s
self
f
a
before:
p
s
f
a
after:
p1
s1
self
f
f
before:
f
after:
p2
s2
p1
s1
p2
s2
h
h

## Slide 40: Explicit List: Summary
Comparison to implicit list:
  Allocate is linear time in number of free blocks instead of total blocks – much faster allocates when most of the memory is full
  Slightly more complicated allocate and free since needs to splice blocks in and out of the list
  Requires space for the links (potentially increases the minimum block size)
Main use of linked lists is in conjunction with segregated free lists (upcoming Method 3)
  Keep multiple linked lists of different size classes, or possibly for different types of objects

## Slide 41: Keeping Track of Free Blocks
Method 1: Implicit list using lengths – links all blocks
Method 2: Explicit list among the free blocks using pointers within the free blocks
Method 3: Segregated free list
  Different free lists for different size ranges
Method 4: Blocks sorted by size
  Can use a balanced binary search tree where a node contains the head of an explicit list of free blocks of a single size and that size is used as the key
5
4
2
6
5
4
2
6

## Slide 42: Segregated Storage
Each size range has its own free list of blocks
1-2
3
4
5-8
9-16
  Often separate lists for small sizes (3,4)
  Larger sizes typically grouped into powers of 2

## Slide 43: Simple Segregated Storage
A free list and collection of pages for each size range
To allocate a block of size n:
  If free list for size n is not empty,
    Allocate first block on list (list can be implicit or explicit)
      Requirement: The size of every block in the free list is equal to the upper end of the range
  If free list is empty,
    Get a new page
    Create new free list from all blocks in page
    Allocate first block on list
  No splitting
To free a block:
  Add to free list
  Instead of coalescing, if page is empty, return the page for use by another size
Tradeoffs:
  Fast (constant time allocate/free), but can fragment badly
  Interesting observation: approximates a best fit placement policy without having the search entire free list

## Slide 44: Segregated Fits
Array of free lists, each list for some size range
To allocate a block of size n:
  Search appropriate free list for block of size m >= n
  If an appropriate block is found:
    Split block and place fragment on appropriate list (optional)
  If no block is found, try next larger size range
  Repeat until block is found
To free a block:
  Coalesce (optional) and place on appropriate free list

## Slide 45: Segregated Fits (continued)
Unlike Simple Segregated Storage, each list may contain blocks of different sizes (that fall within the range)
  Unlike Simple Segregated Storage searching the appropriate free list for a block may require iterating over the entire list
    The list can be long, and so the search can be slow
    More and smaller size ranges my help
  However, allocation from a larger size range can always use the first block in the list, if the list isn't empty
Tradeoffs
  Faster search than all previous methods except simple segregated storage
    Can guarantee log time for power of two size ranges
  Controls fragmentation of simple segregated storage
  Coalescing can increase search times
    Deferred coalescing can help

## Slide 46: Keeping Track of Free Blocks
Method 1: Implicit list using lengths – links all blocks
Method 2: Explicit list among the free blocks using pointers within the free blocks
Method 3: Segregated free list
  Different free lists for different size ranges
Method 4: Blocks sorted by size
  Can use a balanced binary search tree where a node contains the head of an explicit list of free blocks of a single size and that size is used as the key
5
4
2
6
5
4
2
6

## Slide 47: Blocks Sorted by Size
Use a balanced binary search tree (BBST) with the block size as the search key
  The data stored in each tree node is the head of a free list containing blocks of a single size
Allocate and free search for the tree node holding blocks of the required size
  Why use a BBST instead of a hash table? …
  If that node doesn’t exist ...
    Allocate searches for the node whose free list holds blocks of the next larger size
    Free creates a new tree node whose free list can hold the block

## Slide 48: Blocks Sorted by Size: +’s and –’s
Inherently achieves best fit (“+”)
Relies on programs only allocating objects of a few different sizes (“-”)
  Otherwise, even logarithmic time operations will take longer than segregated fits
Implementation complexity (“-”)

## Slide 49: Other Goals: Spatial Locality
Most techniques give little control over spatial locality
  Sequentially-allocated blocks not necessarily adjacent
  Similarly-sized blocks (e.g., for same data type) not necessarily adjacent
Would like a series of similar-sized allocations and deallocations to reuse same blocks
  Splitting & coalescing tend to reduce locality
Of techniques seen, which best for spatial locality?
?
?
Simple segregated lists
Each page only has similar-sized blocks

## Slide 50: Spatial Locality: Regions
One technique to improve spatial locality
Dynamically divide heap into mini-heaps
  Programmer-determined
Allocate data within appropriate region
  Data that is logically used together
  Increase locality
  Can quickly deallocate an entire region at once
Changes API
malloc() and free()
must take a region
as an argument

## Slide 51: Implementation Summary
Many options:
  Data structures for keeping track of free blocks
  Block choice policy
  Splitting & coalescing policies
No universal best option
  Many tradeoffs
  Depends on a program’s pattern of allocation and deallocation

## Slide 52: Explicit Memory Allocation/Deallocation
+ Usually low time- and space-overhead
- Challenging to use correctly by programmers
  - Lead to crashes, memory leaks, etc.

## Slide 53: Implicit Memory Deallocation
+ Programmers don’t need to free data explicitly, easy to use
+ Some implementations could achieve better spatial locality and less fragmentation in the hands of your average programmer
- Price to pay: depends on implementation
But HOW could a memory manager know when to deallocate data without instruction from programmer?

## Slide 54: Implicit Memory Management: Garbage Collection
Garbage collection: automatic reclamation of heap-allocated storage – application never has to free
Common in functional languages and modern object oriented languages:
  C#, Go, Java, Lisp, Python, Scala, Swift
Variants (conservative garbage collectors) exist for C and C++
  Cannot collect all garbage
void foo() {
int *p = malloc(128);
return; /* p block is now garbage */
}

## Slide 55: Garbage Collection
How does the memory manager know when memory can be freed?
  In general we cannot know what is going to be used in the future since it depends on conditionals
  But we can tell that certain blocks cannot be used if there are no pointers to them
Need to make certain assumptions about pointers
  Memory manager can distinguish pointers from non-pointers
  All pointers point to the start of a block
  Cannot hide pointers (e.g., by coercing them to an int, and then back again)

## Slide 56: Classical GC algorithms
Reference counting (Collins, 1960)
  Does not move blocks
Mark and sweep collection (McCarthy, 1960)
  Does not move blocks (unless you also “compact”)
Copying collection (Minsky, 1963)
  Moves blocks (compacts memory)
For more information, see Jones and Lin, “Garbage Collection: Algorithms for Automatic Dynamic Memory”, John Wiley & Sons, 1996.

## Slide 57: Memory as a Graph
  Each data block is a node in the graph
  Each pointer is an edge in the graph
  Root nodes: locations not in the heap that contain pointers into the heap (e.g. registers, locations on the stack, global variables)
Root nodes
Heap nodes
unreachable (garbage)
reachable

## Slide 58: Reference Counting
Overall idea
  Maintain a free list of unallocated blocks
  Maintain a count of the number of references to each allocated block
  To allocate, grab a sufficiently large block from the free list
  When a count goes to zero, deallocate it

## Slide 59: Reference Counting: More Details
Each allocated block keeps a count of references to the block
  Reachable  count is positive
  Compiler inserts counter increments and decrements as necessary
  Deallocate when count goes to zero
Typically built on top of an explicit deallocation memory manager
  All the same implementation decisions as before
  E.g., splitting & coalescing
3

## Slide 60: Reference Counting: Example
a = cons(10,empty)
b = cons(20,a)
a = b
b = …
a = …

## Slide 61: Reference Counting: Example
a = cons(10,empty)
b = cons(20,a)
a = b
b = …
a = …
1
10
a

## Slide 62: Reference Counting: Example
a = cons(10,empty)
b = cons(20,a)
a = b
b = …
a = …
2
10
a
b
1
20

## Slide 63: Reference Counting: Example
a = cons(10,empty)
b = cons(20,a)
a = b
b = …
a = …
1
10
a
b
2
20

## Slide 64: Reference Counting: Example
a = cons(10,empty)
b = cons(20,a)
a = b
b = …
a = …
1
10
a
1
20

## Slide 65: Reference Counting: Example
a = cons(10,empty)
b = cons(20,a)
a = b
b = …
a = …
1
10
0
20

## Slide 66: Reference Counting: Example
a = cons(10,empty)
b = cons(20,a)
a = b
b = …
a = …
0
10

## Slide 67: Reference Counting: Example
a = cons(10,empty)
b = cons(20,a)
a = b
b = …
a = …

## Slide 68: Reference Counting: Problem
? What’s the problem? ?
1
No other pointer to this data, so can’t refer to it
  Count not zero, so never deallocated
  Following does NOT hold: Count is positive  reachable
Can occur with any cycle

## Slide 69: Reference Counting: Summary
Disadvantages:
  Managing & testing counts is generally expensive
    Can optimize
  Doesn’t work with cycles!
    Approach can be modified to work, with difficulty
Advantage:
  Simple
    Easily adapted, e.g., for parallel or distributed GC
Useful when cycles can’t happen
  E.g., UNIX hard links

## Slide 70: GC Without Reference Counts
If don’t have counts, how to deallocate?
Determine reachability by traversing pointer graph directly
  Stop user’s computation periodically to compute reachability
  Deallocate anything unreachable

## Slide 71: Mark & Sweep
Overall idea
  Maintain a free list of unallocated blocks
  To allocate, grab a sufficiently large block from free list
  When no such block exists, GC
    Should find blocks & put them on free list

## Slide 72: Mark & Sweep: GC
Follow all pointers, marking all reachable data
  Use depth-first search
  Data must be tagged with info about its type, so GC knows its size and can identify pointers
  Each piece of data must have a mark bit
    Can alternate meaning of mark bit on each GC to avoid erasing mark bits
Sweep over all heap, putting all unmarked data into a free list
  Again, same implementation issues for the free list

## Slide 73: Mark & Sweep: GC Example
Root pointers:
Heap:
Assume fixed-sized, single-pointer data blocks, for simplicity.
Unmarked=
Marked=

## Slide 74: Mark & Sweep: GC Example
Root pointers:
Heap:
Unmarked=
Marked=

## Slide 75: Mark & Sweep: GC Example
Root pointers:
Heap:
Unmarked=
Marked=

## Slide 76: Mark & Sweep: GC Example
Root pointers:
Heap:
Unmarked=
Marked=

## Slide 77: Mark & Sweep: GC Example
Root pointers:
Heap:
Unmarked=
Marked=

## Slide 78: Mark & Sweep: GC Example
Root pointers:
Heap:
Unmarked=
Marked=

## Slide 79: Mark & Sweep: GC Example
Root pointers:
Heap:
Unmarked=
Marked=

## Slide 80: Mark & Sweep: GC Example
Root pointers:
Heap:
Unmarked=
Marked=

## Slide 81: Mark & Sweep: GC Example
Root pointers:
Heap:
Unmarked=
Marked=

## Slide 82: Mark & Sweep: GC Example
Root pointers:
Heap:
Unmarked=
Marked=
Free list:

## Slide 83: Mark & Sweep: Summary
Advantages:
  No space overhead for reference counts
  No time overhead for reference counts
  Handles cycles
Disadvantage:
  Noticeable pauses for GC

## Slide 84: Stop & Copy
Overall idea:
  Maintain From and To spaces in heap
  To allocate, get sequentially next block in From space
    No free list!
  When From space full, GC into To space
    Swap From & To names

## Slide 85: Stop & Copy: GC
Follow all From-space pointers, copying all reachable data into To-space
  Use depth-first search
  Data must be tagged with info about its type, so GC knows its size and can identify pointers
Swap From-space and To-space names

## Slide 86: Stop & Copy: GC Example
Root pointers:
From:
Uncopied=
Copied=
Assume fixed-sized, single-pointer data blocks, for simplicity.
To:

## Slide 87: Stop & Copy: GC Example
Root pointers:
From:
Uncopied=
Copied=
To:

## Slide 88: Stop & Copy: GC Example
Root pointers:
From:
Uncopied=
Copied=
To:

## Slide 89: Stop & Copy: GC Example
Root pointers:
From:
Uncopied=
Copied=
To:

## Slide 90: Stop & Copy: GC Example
Root pointers:
From:
Uncopied=
Copied=
To:

## Slide 91: Stop & Copy: GC Example
Root pointers:
From:
Uncopied=
Copied=
To:

## Slide 92: Stop & Copy: GC Example
Root pointers:
From:
Uncopied=
Copied=
To:

## Slide 93: Stop & Copy: GC Example
Root pointers:
From:
Uncopied=
Copied=
To:

## Slide 94: Stop & Copy: GC Example
Root pointers:
From:
Uncopied=
Copied=
To:

## Slide 95: Stop & Copy: GC Example
Root pointers:
From:
Uncopied=
Copied=
To:

## Slide 96: Stop & Copy: GC Example
Root pointers:
To:
From:
Next block to allocate

## Slide 97: Stop & Copy
Advantages:
  Only one pass over data
  Only touches reachable data
  Little space overhead per data item
  Very simple allocation
  “Compacts” data
  Handles cycles
Disadvantages:
  Noticeable pauses for GC
  Double the basic heap size

## Slide 98: Compaction
Moving allocated data into contiguous memory
Eliminates fragmentation
Tends to increase spatial locality
Must be able to reassociate data & locations
  Not possible if C-like pointers in source language

## Slide 99: GC Variations
Many variations on these three main themes
  Concurrent GC, which does not stop the computation during GC
  Generational GC, which exploits the observation that most objects have a short lifetime
  Conservative GC
Combinations of these three main themes are common
  Java uses both Copying and Mark-and-Sweep within a Generational GC

## Slide 100: Conservative GC
Goal
  Allow GC in C-like languages
Usually a variation on Mark & Sweep
Must conservatively assume that integers and other data can be cast to pointers
  Compile-time analysis to see when this is definitely not the case
  Code style heavily influences effectiveness

## Slide 101: GC vs. malloc/free Summary
Safety is not programmer-dependent
Compaction generally improves locality
Higher or lower time overhead
  Generally less predictable time overhead
Generally higher space overhead

## Slide 102: Next Time
Virtual Memory