## Slide 1
Project Motivation:
The group investigated the McAulay-Quatieri algorithm for sinusoidal representation of signals. A crude speech synthesis model was adapted to implement the McAulay-Quatieri algorithm.
Future Development
Signal compression
Improvement of wavelet algorithm
Decrease distortion
Timbre modification of an acoustic signature
Goals:
Divide signal into frequency tracks
Use frequency matching to synthesize signal
  Alter signal duration
  Preserve frequency content
Applications:
Medical signal analysis
Aid for musical development
Altering timbre within MIDI fonts
Fourier Transform Approach
Signal divided into Hamming windows
Short time Fourier transform (STFT) performed on each window
Frequency tracks used for signal synthesis
Wavelet Approach
Wavelet Motivation
Fourier analysis not always optimal
Wavelet transform provides alternative
Technique emphasizes edge detection
Wavelet Method
Haar wavelet basis
Coefficients are grouped by the Scale index
Position index used as an analogue to phase
Edges in bases correspond to frequency
Fourier techniques applied to wavelet coefficients
  McAulay-Quatieri algorithm adapted
  New coefficients interpolated
Signal synthesized
Sources
McAulay, Robert and Thomas Quatieri. Speech Analysis/ Synthesis Based on a Sinusoidal Representation. IEEE Transactions on Acoustics, Speech, and Signal Processing. Aug. 1986.
Lemur Website: http://www.cerlsoundgroup.org/Kelly/ICMC95/TimbreManipulationTool.html
DSP Projects Site: http://www.owlnet.rice.edu/~elec431/projects96/finest/elec431_report.html
Frequency Tracking
Speech Model:
Discrete frequency peaks
  Migrate over time
  Appear and die out
  Lifetimes modeled as tracks
Track creation:
Highest power STFT peaks selected
  Amplitude, phase and frequency recorded
  Selection of more peaks yield less distortion but higher computation time.
Peak matched to closest peaks in adjacent frames
Interpolation:
New frequencies generated in tracks
Amplitude interpolated linearly
Phase interpolated cubically
Synthesis:
New samples generated from interpolated data
Signal recreated from synthesized samples
The original signal, a constant frequency sine wave
Track history of sin [0.005 * n2]
  Highest power peaks taken from each sample
  Depiction of peak migration over time
Reconstructed Signal
  Interpolated data used
    Duration increased
    Frequency maintained
  Success! 